Assess Yourself

Score yourself out of 12

Multiple Choice (6 points)

- A parallel plate capacitor is connected to a battery of potential V. The distance between the plates is doubled without disconnecting the battery. Which of the following is true?

  - Both the capacitance and the charge on the plates are decreased by one-half.

  - The capacitance is decreased by one half, but the charge on the plate is unchanged.

  - The capacitance is unchanged, but the charge on the plates is decreased by one-half.

  - The capacitance is doubled, and the charge on the plates is unchanged.

  - Both the capacitance and the charge on the plates are doubled.

- Two large, flat, parallel, conducting plates are 0.04 m apart. The lower plate is at a potential of 2 V with respect to ground. The upper plate is at a potential of 10 V with respect to the ground. Point P is located 0.01m above the lower plate. What is the electric potential at point P?

  - 10 V

  - 8 V

  - 6 V

  - 4 V

  - 2 V

- A point P is 0.50 meter from a point charge of 5.0 X 10^-8 coulomb.

  - 2.5*10^-8 V

  - 2.5*10^1 V

  - 9.0*10^2 V

  - 1.8*10^3 V

  - 7.5*10^3 V

Two positive charges of magnitude q are each a distance d from the origin A of a coordinate system as shown above. At which of the following points is the electric potential greatest in magnitude

  - A

  - B

  - C

  - D

  - E

- The capacitance of a parallel-plate capacitor can be increased by increasing which of the following?

  - The distance between the plates

  - The charge on each plate

  - The area of the plates

  - The potential difference across the plates

  - None of the above

- An electron volt is a measure of

  - energy

  - electric field

  - electric potential

  - force

  - electric charge

Free Response (6 points)

Two charges are situated as shown. The distances are given in the drawing. The charges have the following values: q1 is 5.0 (C and q2 is -2.0 (C.

(a) Find the potential difference at point P.

(b) How much work is required to bring a third point charge of 4.0 (C from infinity to P?