| Chapter 15: The Laws of Thermodynamics Practice Questions |  |
| --- | --- |

Top of Form

|  | The process shown above is called |
| --- | --- |
|  | isobaric process. |
|  | isochoric process. |
|  | isothermal process. |
|  | adiabatic process. |
|  | 2. The process shown above is called |
|  | isobaric process. |
|  | isochoric process. |
|  | isothermal process. |
|  | adiabatic process. |
|  | 3. The process shown above is called |
|  | isobaric process. |
|  | isochoric process. |
|  | isothermal process. |
|  | adiabatic process. |
|  | 4. In the above figure, the volume at point "a" is 200 L and the pressure is 5 atm.The pressure at "b" is 1 atm. What is the work done? |
|  | 80000000 J |
|  | 400000 J |
|  | 80000 J |
|  | 0 J |
|  | 5. In the above figure, the volume at point "a" is 200 L and the pressure is 5 atm. The volume at "b" is 400 L. What is the work done? |
|  | 2x108 J |
|  | 1x108 J |
|  | 1x105 J |
|  | 0 J |
|  | 6. In the above figure, the volume at point "c" is 800 L and the pressure is 2 atm. The volume at "d" is 400 L. What is the work done? |
|  | 8x107 J |
|  | 8x105 J |
|  | -8x107 J |
|  | -8x105 J |
|  | 7. In the above figure, the volume at point "c" is 800 L and the pressure is 2 atm. The volume at "a" is 400 L and the pressure is 5 atm. What is the work done as the system goes through one complete cycle abcd? |
|  | 800000 J |
|  | 400000 J |
|  | 280000 J |
|  | 120000 J |
|  | 8. In the above figure, the volume at point "c" is 800 L and the pressure is 2 atm. The volume at "a" is 400 L and the pressure is 5 atm. What heat is absorbed by the system in the above square cycle? |
|  | 120000 J |
|  | 0 J |
|  | -120000J |
|  | Not enough information. |
|  | 9. In the above figure, QH is 10000 J and QC is 6000 J. What is the efficiency? |
|  | .6 |
|  | .55 |
|  | .4 |
|  | Need more information. |
|  | 10. If the heat engine above is a Carnot engine, and QH is 10000J, what is W? |
|  | 4500 J |
|  | 5500 J |
|  | 6500 J |
|  | 7500 J |
|  | 11. What is the coefficient of performance (CP) of the reversible (Carnot) refrigerator shown above? |
|  | .1 |
|  | 9 |
|  | 10 |
|  | 11 |
|  | 12. What is the coefficient of performance (CP) of the reversible (Carnot) heat pump shown above? |
|  | .1 |
|  | 9 |
|  | 10 |
|  | 11 |
|  | 13. The heat engine shown above is |
|  | a reversible (Carnot) heat engine. |
|  | an irreversible heat engine. |
|  | a hoax. |
|  | none of the above. |
|  | 14. The heat engine shown above is |
|  | a reversible (Carnot) heat engine. |
|  | a irreversible (Carnot) heat engine. |
|  | a hoax. |
|  | none of the above. |
|  | 15. A reservoir delivers 1000 J of heat to another reservoir at 133 oC. What is the increase in entropy of the second reservoir? |
|  | 7.52 J/K |
|  | 2.5 J/K |
|  | 1000 J/K |
|  | 133000 J/K |