Temperature and Kinetic Theory Practice: Answers

- C – an increase in temperature would result in an increase in diameter

- C – the gauge pressure is 2 atm, so the absolute pressure is 3 atm. If the temperature is doubled, pressure would also double. The absolute pressure will be 6 atm, and gauge pressure 5 atm.

- B – using the ideal gas law: T = PV/(nR) = 100000Pa*0.02m3/(1mol*8.3J/mol*K) = 240.96 K

- D – At STP, P=1atm and T=0°C

PV=nRT

V=nRT/P=(1mol)(0.08206L*atm/mol*K)(273K)/(1atm)

V=22.4L

- B – PV=nRT

n=PV/(RT)=(101325N/m2)(5*3*2.5m3)/[(8.31J/mol*K)(273K)]

n=1675mol=1700mol

- Using KE=3/2kT:

1/2mv2=3/2kT

v=(3kT/m)1/2 =(3RT/M)1/2  (multiply top and bottom by NA)

=(3(8.31J/mol*K)(300K)/(0.002kg/mol))1/2

v=1934m/s

- Linear expansion:

L-Lo=αLoΔT

16.05cm – 16.1cm=(19x10-6/°C)(16.1cm) ΔT

ΔT=-163°C or it needs to be cooled by 163°C

- ΔV=βVoΔT, V= Vo(1+βoΔT)

ρ=m/V, V=m/ρ

m/ρ= m/ρo(1+βoΔT)

ρ= ρo/(1+βoΔT)=(1.00*103kg/m3)/(1 + (210x10-6/°C)(94°C - 4°C))

=981.45 kg/m3

- Each piece can expand by:

ΔL=αLoΔT = (22.2*10-6/°C)(3.6m)(55°C) = 0.0044m

If each piece can expand in both directions, then each will expand 0.0022m toward the other. The gap should be at least 2*0.0022m = 0.0044m to keep the pieces from buckling.

- a) M = m/n  (M = molar mass)

n = m/M

5kg / (0.044kg/mol) = n = 113.64 mol of CO2

T = PV/(nR) = (2.0*105 Pa)(0.50 m3)/(113.64mol*8.31J/mol*K)

T=106K

b) P1V1=P2V2

P2= V1/ V2*P1

=(0.5 m3/0.75 m3) * 2*105Pa

=1.3*105Pa

- Use Boyle’s law: P1V1=P2V2

P1Ah1=P2Ah2

P1h1=P2h2

h2 = P1/P2*h1

=130kPa/170kPa * 25cm

=19.1cm

- The change in temperature is ΔT=31°C - 6°C = 25°C.

- For a square with side length s, A=s2

Δs=αsΔT

ΔA=2sΔs=(2s)(αsΔT)  (assuming for small changes in s, (Δs)2=0)

ΔA=2αs2ΔT

ΔA=2αAoΔT (A=s2)